## Slide 1
Computer Networking

## Slide 2: Chapter 1: Computer Networks and the Internet
Overview/roadmap:
What is the Internet?
What is a protocol?
The Network edge: hosts, access network, physical media
The Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History of Computer Networking and the Internet

## Slide 3: How do packet loss and delay occur?
packets queue in router buffers
packets queue, wait for turn
arrival rate to link (temporarily) exceeds output link capacity: packet loss
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 4: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 5: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
* Check out the online interactive exercises: http://gaia.cs.umass.edu/kurose_ross

## Slide 6: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Suppose Computer A sends a message to a server:
The router receives the packet → checks the header → takes a few microseconds (processing delay).
If other packets are waiting to be sent, the packet waits in queue for some time (queueing delay).
Then, the packet is transmitted bit-by-bit over the cable (transmission delay).
Finally, it travels physically across the network to the destination (propagation delay).
Each delay adds up to the total time it takes for the packet to go from A to B.

## Slide 7: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km

## Slide 8: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 9: Packet queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1

## Slide 10: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 11: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic link
* Do some traceroutes from exotic countries at www.traceroute.org
looks like delays decrease! Why?
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu

## Slide 12: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 13: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 14: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 15: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/

## Slide 16: Chapter 1: Computer Networks and the Internet
Overview/roadmap:
What is the Internet?
What is a protocol?
The Network edge: hosts, access network, physical media
The Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History of Computer Networking and the Internet

## Slide 17: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 18: Bad guys: malware
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam or distributed denial of service (DDoS) attacks

## Slide 19: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts

## Slide 20: Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Wireshark software used for our end-of-chapter labs is a (free) packet-sniffer

## Slide 21: Bad guys: fake identity
IP spoofing: send packet with false source address
A
B
C
… lots more on security (throughout, Chapter 8)
src:B dest:A payload

## Slide 22: Chapter 1: Computer Networks and the Internet
Overview/roadmap:
What is the Internet?
What is a protocol?
The Network edge: hosts, access network, physical media
The Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History of Computer Networking and the Internet

## Slide 23: Protocol “layers” and reference models
Networks are complex, with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software

## Slide 24: Example: organization of air travel
airline travel: a series of steps, involving many services
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 25: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
Q: describe in words the service provided in each layer above

## Slide 26: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?
layering in other complex systems?

## Slide 27: ISO/OSI reference model
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model

## Slide 28: Internet protocol stack
application: supporting network applications
  IMAP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 29: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 30: Chapter 1: Computer Networks and the Internet
Overview/roadmap:
What is the Internet?
What is a protocol?
The Network edge: hosts, access network, physical media
The Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History of Computer Networking and the Internet

## Slide 31: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 32: Internet history
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
1972-1980: Internetworking, new and proprietary nets
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best-effort service model
  stateless routing
  decentralized control
define today’s Internet architecture

## Slide 33: Internet history
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 34: Internet history
early 1990s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990s: commercialization of the Web
late 1990s – 2000s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000s: commercialization, the Web, new applications

## Slide 35: Internet history
~18B devices attached to Internet (2017)
    rise of smartphones (iPhone: 2007)
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access: 4G/5G, WiFi
emergence of online social networks:
  Facebook: ~ 2.5 billion users
service providers (Google, FB, Microsoft) create their own networks
    bypass commercial Internet to connect “close” to end user, providing “instantaneous” access to search, video content, …
enterprises run their services in “cloud” (e.g., Amazon Web Services, Microsoft Azure)
2005-present: more new applications, Internet is “everywhere”

## Slide 36: Chapter 1: summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!